## Slide 1
Network Security Fundamentals & FortiGate Integration
Building a Resilient, Segmented, and Secured Network Environment
Date November 25, 2025
PAGE 1

## Slide 2
PAGE 2
Prepared By :
Mostafa Hossam eldein Ebrahem
Sara Hatem Mohamed
Rawda Ayman Saad Rashed
Omar Adil Selim
Shaza Muhmad Sofy Abdelwahed

## Slide 3
PAGE 3
Project Overview
Project Name: Network Security Fundamentals and FortiGate Integration Goal: Build a secure and segmented network using FortiGate Firewall Focus Areas:
Threat analysis FortiGate deployment NAT & Firewall policies

## Slide 4
2.
PAGE 4
Project Goals & Objectives
1.
GOALS:
Establish a strong security posture Deploy a secure NGFW environment Control inbound and outbound traffic
OBJECTIVES:
Analyze cyber threats Configure FortiGate VM Implement NAT & Firewall rules

## Slide 5
PAGE 5
WEEK 1 Network Security Fundamentals
Major Threats
  Phishing & Social Engineering
  Malware (Ransomware, Viruses, Worms)
  DoS/DDoS Attacks
  Man-in-the-Middle (MitM)
  Insider Threats
Key Vulnerabilities
  Weak / Reused Passwords
  Unpatched Systems
  Misconfigurations

## Slide 6
PAGE 6
CIA Triad
→ Confidentiality Encryption + Strong/MFA/Biometric Auth
→ Integrity Hashing + Backups + Permissions
→ Availability Redundancy + Disaster Recovery

## Slide 7
PAGE 7
Countermeasures & WannaCry Lesson
Essential Protections
  User Training
  Regular Patching + Antivirus
  HTTPS + VPN (vs MitM)
  DDoS Protection
  Least Privilege + Monitoring
WannaCry 2017
→ Exploited unpatched Windows (EternalBlue)
Key Lesson: Patch fast + Layered defense + Awareness

## Slide 8
PAGE 8
WEEK 2 FortiGate Deployment & Initial Configuration
  Nework Topology used
  FortiGate dashboard overview
  Static & Dynamic interfaces
  Routing Table Review
  Initial firewall policies before applying
any advance filtering

## Slide 9
Network Topology
PAGE 9
Shows the overall network design used in the FortiGate setup
( WAN, LAN segments, internal interfaces, and how devices are interconnected. It visualizes the logical flow of traffic through the firewall.)

## Slide 10
FortiGate Dashboard Overview
PAGE 10
  Shows system status
  Displays resource usage
(CPU, RAM, sessions)
  Shows interface connectivity status
  Provides real-time traffic visibility
  Alerts and security logs

## Slide 11
PAGE 11
Static Network Interfaces
  Configured internal LAN interfaces manually
  Assigned IP addresses required for internal network communication
  Set administrative access (HTTP/HTTPS/SSH) for management
  Ensured links were active so the firewall could communicate with internal devices
  This step created the foundation for routing and future policies

## Slide 12
PAGE 12
Static Network Interfaces

## Slide 13
PAGE 13
Dynamic Network Interface
  Configured the WAN port to obtain its IP automatically (DHCP)
  Verified the public IP assigned by the ISP/router
  Ensured internet connectivity was working
  This interface is what allows the firewall to reach the outside world
  Critical step before creating NAT or security policies

## Slide 14
PAGE 14
Dynamic Network Interface

## Slide 15
PAGE 15
Verified the routing table: default route to WAN + LAN routes correctly listed.
Ensured no missing or conflicting routes, confirming proper traffic flow to LAN and internet
Routing Table Review

## Slide 16
Initial Firewall Policy
  Confirmed which traffic is allowed (between Branch and HQ)
  Reviewed the source and destination interfaces used by the VPN tunnel.
  Checked the rule order and implicit deny to understand the full traffic flow.
PAGE 16

## Slide 17
PAGE 17
Week 2 Summary
  Built the initial FortiGate setup and verified system readiness
  Configured static LAN and dynamic WAN interfaces
  Validated internal/external connectivity through routing checks
  Reviewed initial firewall policies and default traffic flow
  Ensured the network is structured and prepared for next security phases

## Slide 18
PAGE 18
WEEK 3
Advanced Policies & NAT Implementation
  Configured firewall policies for VLANs and VPN.
  Enabled secure internet access for Staff and Guests.
  Implemented HQ ↔ Branch site‑to‑site VPN.
  Validated NAT, routing, and DHCP functionality.

## Slide 19
PAGE 19
Network Topology Overview
Shows HQ VLANs, Branch link, and WAN connection.
Highlights the path of internal and VPN traffic.

## Slide 20
PAGE 20
Policy ID 3 – Staff Internet
  Allows VLAN 20 to access internet through WAN.
  NAT enabled; security profiles applied.
  Covers HTTP/HTTPS/DNS

## Slide 21
PAGE 21
Policy ID 4 – Branch-to-HQ Local Traffic
Allows return traffic from Branch to HQ via VPN.
NAT disabled to preserve internal addressing.
“Required for full two‑way VPN connectivity”

## Slide 22
PAGE 22
Policy ID 5 – HQ-to-Branch Communication
Staff VLAN can access Branch through VPN tunnel.
All services allowed; security inspection enabled.
Core rule for site‑to‑site connectivity.

## Slide 23
PAGE 23
Policy ID 6 – Staff Access to Servers
VLAN 20 allowed to reach VLAN 40 for restricted services.
FTP, MySQL, RADIUS enabled.
Security and NAT applied.

## Slide 24
PAGE 24
Policy ID 7 – Guests Internet Access
  Guests (VLAN 30) allowed limited internet access.
  Only DNS, HTTP, HTTPS, PING allowed.
  Strict inspection applied.

## Slide 25
PAGE 25
Session Table & VPN Verification
  Shows active sessions across VLANs (Staff, Guests, Servers).
  ICMP entries confirm successful inter-VLAN connectivity.
  DHCP broadcasts show devices receiving IPs normally.
  SNAT is active → internal IPs are translated to the firewall’s WAN IP when going to the internet.
  DNAT is active → firewall handles traffic coming from outside into internal networks.
  UDP/500 session indicates an active IPsec VPN negotiation.

## Slide 26
PAGE 26
Session Table & VPN Verification

## Slide 27
First DHCP attempt failed (interface initializing).
Second attempt completed DORA cycle.
Guest2 received valid IP and gateway.
DHCP Validation – Guest Network
PAGE 27

## Slide 28
PAGE 28
Week 3 Summary
  All VLANs were configured and linked through secure, well-defined firewall policies.
  Internet access for Staff and Guests works with proper filtering and NAT.
  Site-to-site VPN between HQ and Branch is fully functional and verified.
  Internal services are protected through controlled access rules.
  DHCP, NAT, routing, and session handling were successfully validated.
“The network is stable, secure, and operating exactly as designed”

## Slide 29
PAGE 29
Compiled all project findings from Week 1 to Week 3
Organized configuration steps, policies, NAT rules, and screenshots
Week 4
Presentation & Final Report
Structured a professional presentation summarizing:
Threat analysis FortiGate configuration Policies & NAT Testing
Ensured all tasks meet the project requirements and learning objectives

## Slide 30
PAGE 30
We sincerely appreciate your time and the opportunity to present our work.
This project has been a valuable experience for us to grow technically and professionally as future security engineers.
Thank you for your guidance and support
Thank You